## Slide 1
BTS3911E 关键规格 | 
Frequency Band | 1.8G(L)+2.1G(U/L)
 | 1.8G:1735~1780MHz；1830~1875MHz
 | 2.1G:1920~1980MHz；2110~2170MHz
Output Power | 2*10W
IBW | 40MHz
Maximum Cells | Uo: 4UMTS；
 | Lo: 2x20MHz LTE+1x20MHz LTE；
 | UL: 4UMTS+1x20MHz LTE；
Capacity | Uo: 512CE
 | Lo: 600 RRC-connected user per cell
 | 1200 RRC-connected user per site
 | UL: 256CE+600 RRC-connected user per site
Antenna | Internal/External
GPS | Internal
Dimensions | ~10L (external antenna)
Weight | ~10Kg (external antenna)
Input Power | AC
Transmission Interface | 2 FE/GE+2 SFP*
Operating Temperature | -40℃ ～ +50℃
IP Environmental Ratings | IP65
BTS3911E
一体化站点解决方案
支持UL平滑演进，降低CAPEX
采用SDR技术，可通过软件配置实现UMTS only, FDD LTE only, UL三种模式，支持U向L平滑演进
2*10W大功率，支持动态功率共享，满足不同场景应用，节省运营商投资
硬件Ready，无缝拼接支持Wi-Fi模块扩展，满足热点区域数据分流需求
小站点，大容量，提升用户体验
容量大：LTE only最大支持1200个RRC连接用户数；UMTS only最大支持384个 HSPA用户
吞吐量高：LTE only单站最大吞吐量下行450Mbps，上行225Mbps；UMTS only单站最大吞吐率下行168Mbps，上行46Mbps
LTE only场景，支持2*20M 频段内和频段间CA，提升系统容量和用户体验
高集成度 ，降低部署成本
高集成度，内置2光/2电传输接口，支持PoE输出供电，节省传输和部署成本
CPRI光口设计，硬件Ready可支持RRU扩展，提供多样化组网方案
一体化设计，体积小、重量轻、易维护，支持挂墙，抱杆等多种安装方式，降低站点租赁费用
3911E是华为新推出可支持UMTS&LTE多模多频的一体化微基站。3911E体积小、重量轻、即插即用、自配置、无需Shelter和机房的特点，在站址获取及工程部署上具有极大的优势，为运营商提供快速便捷的站点解决方案。

## Slide 2
BTS3911E DATA SHEET | 
Frequency Band | 1.8G(L)+2.1G(U/L)
 | 1.8G:1735~1780MHz；1830~1875MHz
 | 2.1G:1920~1980MHz；2110~2170MHz
Output Power | 2*10W
IBW | 40MHz
Maximum Cells | Uo: 4 cells；
 | Lo: 2 cells x20MHz LTE+1x20MHz LTE；
 | UL: 4 UMTS cells+1 LTE cell
Capacity | Uo: 512CE
 | Lo: 600 RRC-connected user per cell
 | 1200 RRC-connected user per site
 | UL: 256CE+600 RRC-connected user per site
Antenna | Internal/External
GPS | Internal
Dimensions | ~10L (external antenna)
Weight | ~10Kg (external antenna)
Input Power | AC
Transmission Interface | 2 FE/GE+2 SFP*
Operating Temperature | -40℃ ～ +50℃
IP Environmental Ratings | IP65
BTS3911E
One Site Solution
Smooth Evolution, Reduce CAPEX
BTS3911E adopts the software-defined radio (SDR) technology so that it can work in different modes (including UMTS Only, LTE Only, and UMTS/LTE dual-mode) to support smooth evolution from UMTS to LTE
BTS3911E support s power sharing between different band to meet different scenarios requirement to save the investment
Hardware ready for Wi-Fi expansion to meet the data requirement in hotspot.
Small Cell & Large Capacity, Improve User Experience
Large capacity: 1200 UEs in radio resource control (RRC) connected mode in LTE Only mode and 384 HSPA UEs in UMTS Only mode in Max.
High throughput: The maximum throughput are 450 Mbit/s in downlink and 225 Mbit/s in uplink in LTE Only mode. In UMTS Only mode, the value are 168 Mbit/s in downlink and 46 Mbit/s in uplink.
2*20M intra-band CA and inter-band CA in LTE only mode improves the system capacity and user experience.
Highly Integrated Structure, Reduce Deployment Cost
Highly integrated structure with 2 electrical or 2 optical ports to provide power in PoE mode saves transmission and deployment cost.
CPRI optical design is ready for RRU expansion to support diversity network requirement.
Small and light-weight, BTS3911E is easy to install and maintain. It can be installed on a wall or pole without the need for an equipment room to reduce costs in site leasing.
BTS3911E is a dual-band UMTS/LTE micro base station. It is small, light-weight, and comes with plug-and-play and self-configuration features, making it an excellent network solution for operators. BTS3911E requires no shelter or equipment room, facilitating site acquisition and network deployment.